## Slide 1
CardioFusion
ECG model progress
Notes: Progress presentation. The ECG encoder predicts HFrEF. Four channels here means the four site recordings grouped for one patient: APEX, LLSB, LUSB and RUSB.
Sources: Untitled document.pdf, pp. 1–6; git 82be782 and 016cfc2, notebooks/2_ecg_baseline.ipynb; current notebooks/2_ecg_baseline.ipynb and notebooks/3_ecg_5second_segments.ipynb; models/ecg_5s/fold0_seed42/comparison.csv. All values are saved experimental results, not clinical performance estimates.

## Slide 2
1. The first model used separate segments
Each site recording was split into five-second segments and treated as a separate input.
Results | AUROC | Accuracy | Precision | Recall | F1
Validation | 0.6858 | 63.8% | 22.0% | 64.2% | 32.8%
Test | 0.7921 | 65.8% | 8.8% | 77.5% | 15.9%
A simple CNN with one input channel.
It caught some HFrEF cases, but produced
too many false alarms.
Test confusion matrix
Actual / predicted | Non-HFrEF | HFrEF
Non-HFrEF | 1802 | 958
HFrEF | 27 | 93
Notes: Experiment 1. AUROC validation 0.6858, test 0.7921. Weighted BCE, 10 epochs. Validation counts TN=1319 FP=751 FN=118 TP=212. Test counts TN=1802 FP=958 FN=27 TP=93. Positive-class F1 is 0.3279196 validation and 0.1588386 test. Metrics are calculated from the counts, with AUROC from notebook outputs. Segment counts are not independent patient counts. The legacy split and unit differ from the later patient split, so the comparison is historical rather than a controlled ablation.
Sources: Untitled document.pdf, pp. 1–6; git 82be782 and 016cfc2, notebooks/2_ecg_baseline.ipynb; current notebooks/2_ecg_baseline.ipynb and notebooks/3_ecg_5second_segments.ipynb; models/ecg_5s/fold0_seed42/comparison.csv. All values are saved experimental results, not clinical performance estimates.

## Slide 3
2. Changes for a four-channel model
Dataset review showed that each patient had four recordings that needed to be used together.
Group APEX, LLSB, LUSB and RUSB by patient ID.
Stack the four 30-second signals into one input.
Change the CNN from one input channel to four.
Add residual convolution blocks and split the data by patient.
Notes: Changes leading to experiment 3: group the four site recordings by patient ID in a fixed channel order; stack four complete 30-second ECG recordings as a single 4 x 15000 input; update the encoder input channels from 1 to 4; use residual convolution blocks and global average/max pooling; keep each patient within one data split. This is a summary of implementation changes, not an isolated causal claim about the contribution of each change.
Sources: Untitled document.pdf, pp. 1–6; git 82be782 and 016cfc2, notebooks/2_ecg_baseline.ipynb; current notebooks/2_ecg_baseline.ipynb and notebooks/3_ecg_5second_segments.ipynb; models/ecg_5s/fold0_seed42/comparison.csv. All values are saved experimental results, not clinical performance estimates.

## Slide 4
3. Four-channel model results
One patient now gives one input: APEX, LLSB, LUSB and RUSB, each with 30 seconds.
Results | AUROC | Accuracy | Precision | Recall | F1
Validation | 0.9564 | 91.0% | 57.9% | 91.7% | 71.0%
Test | 0.9983 | 96.7% | 55.6% | 100.0% | 71.4%
The CNN now takes four channels together.
Deeper residual blocks learn richer features.
The model can combine information from
the same patient across the four sites.
Test confusion matrix
Actual / predicted | Non-HFrEF | HFrEF
Non-HFrEF | 111 | 4
HFrEF | 0 | 5
Notes: Experiment 3. Preprocessing stacks 4 x 15000 ECG samples in a fixed site order. Per-channel filtering and z-score normalization remain. Input channels changed from 1 to 4; residual convolution blocks and global average/max pooling replaced the older small CNN. A patient-based fold split prevents a patient from spanning training and validation. The proposed mechanism is more patient context and a richer encoder, but no ablation isolates which change caused the gain. Validation cutoff .5117487311, TN80 FP8 FN1 TP11. Test TN111 FP4 FN0 TP5. Only 5 positive test patients, so one case changes recall by 20 percentage points. Site labels identify recording sites and are not a claim that these are four standard simultaneous ECG leads.
Sources: Untitled document.pdf, pp. 1–6; git 82be782 and 016cfc2, notebooks/2_ecg_baseline.ipynb; current notebooks/2_ecg_baseline.ipynb and notebooks/3_ecg_5second_segments.ipynb; models/ecg_5s/fold0_seed42/comparison.csv. All values are saved experimental results, not clinical performance estimates.

## Slide 5
4. Training with five-second segments
The four channels stay together. A fresh model learns from six windows per training patient.
Results | AUROC | Accuracy | Precision | Recall | F1
Validation | 0.8845 | 87.0% | 47.6% | 83.3% | 60.6%
Test | 0.9200 | 83.3% | 17.4% | 80.0% | 28.6%
These results use only the first five seconds.
The model still finds useful information,
but false positives rise from 4 to 19
compared with the full 30-second model.
Test confusion matrix
Actual / predicted | Non-HFrEF | HFrEF
Non-HFrEF | 96 | 19
HFrEF | 1 | 4
Notes: Experiment 4. Fresh weights with the same four-channel architecture, not a reshape of the trained 30-second model. Adaptive pooling accepts the shorter input. Raw windows are cropped before filtering and normalization to avoid using later samples in the first-window prediction. Each 30-second record produces 6 non-overlapping five-second windows; incomplete final windows are discarded. Splits are made by patient before windows. Training has 400 patients and 2400 windows. Threshold for single windows .41620755 is selected on validation. First five seconds: validation TP10 FN2 FP11 TN77, test TP4 FN1 FP19 TN96. Lower recording requirement does not establish a measured inference-speed improvement.
Sources: Untitled document.pdf, pp. 1–6; git 82be782 and 016cfc2, notebooks/2_ecg_baseline.ipynb; current notebooks/2_ecg_baseline.ipynb and notebooks/3_ecg_5second_segments.ipynb; models/ecg_5s/fold0_seed42/comparison.csv. All values are saved experimental results, not clinical performance estimates.

## Slide 6
5. Predictions change across segments
Test results for each five-second window, using the same model and cutoff.
All six predictions agree for 96 of 120 patients.
One HFrEF patient changes from negative
in the first three windows to positive
in the last three.
Chart: Window (seconds)
| 0–5 | 5–10 | 10–15 | 15–20 | 20–25 | 25–30
HFrEF F1 | 0.28571 | 0.4 | 0.38095 | 0.41667 | 0.47619 | 0.52632
Results | AUROC | Accuracy | Precision | Recall | F1
0-5s | 0.9200 | 83.3% | 17.4% | 80.0% | 28.6%
5-10s | 0.9357 | 90.0% | 26.7% | 80.0% | 40.0%
10-15s | 0.9670 | 89.2% | 25.0% | 80.0% | 38.1%
15-20s | 0.9635 | 88.3% | 26.3% | 100.0% | 41.7%
20-25s | 0.9739 | 90.8% | 31.2% | 100.0% | 47.6%
25-30s | 0.9896 | 92.5% | 35.7% | 100.0% | 52.6%
Notes: Window-position results are descriptive test analysis, not a basis for choosing a preferred window using test performance. All use a frozen single-window threshold .41620755. Overall agreement is 96/120=80%, including 92 negatives and 4 positives. Agreement does not equal correctness: 5 negative patients are incorrectly positive in all windows. One positive patient is negative in windows 0,1,2 and positive in 3,4,5. The graph plots positive-class F1 with a common 0 to 1 scale. No claim that later windows are universally better.
Sources: Untitled document.pdf, pp. 1–6; git 82be782 and 016cfc2, notebooks/2_ecg_baseline.ipynb; current notebooks/2_ecg_baseline.ipynb and notebooks/3_ecg_5second_segments.ipynb; models/ecg_5s/fold0_seed42/comparison.csv. All values are saved experimental results, not clinical performance estimates.

## Slide 7
6. Averaging segments helps
Comparison of one window, the mean of six window scores, and majority voting.
Chart: Recall
Averaging reduces false positives from 19 to 4.
It still misses one HFrEF case.
Results | AUROC | Accuracy | Precision | Recall | F1
First 5 seconds | 0.9200 | 83.3% | 17.4% | 80.0% | 28.6%
Mean of six (30 s) | 0.9739 | 95.8% | 50.0% | 80.0% | 61.5%
Majority vote (30 s) | 0.9661 | 92.5% | 33.3% | 80.0% | 47.1%
Full 30-second model | 0.9983 | 96.7% | 55.6% | 100.0% | 71.4%
Notes: ROC curves reconstructed from saved patient probabilities. Trapezoidal areas independently verified: .9982608695652174 full30, .92 first5, .9739130434782609 mean6. Native chart data retains every ROC point including ties. Mean6 threshold .546824038; majority uses the single-window threshold and mean6 threshold to break 3–3 ties. Mean6 test TP4 FN1 FP4 TN111; majority TP4 FN1 FP8 TN107; full30 TP5 FN0 FP4 TN111. Improvement in thresholded metrics reflects aggregation and separately validation-selected thresholds, not averaging alone. A 12-second input yields two full windows and discards the final two seconds. Next steps: assess all patient folds and additional seeds, estimate uncertainty with more positive patients, and run matched one-vs-four-channel ablations to separate input grouping from network changes.
Sources: Untitled document.pdf, pp. 1–6; git 82be782 and 016cfc2, notebooks/2_ecg_baseline.ipynb; current notebooks/2_ecg_baseline.ipynb and notebooks/3_ecg_5second_segments.ipynb; models/ecg_5s/fold0_seed42/comparison.csv. All values are saved experimental results, not clinical performance estimates.